## Slide 1: Physics 4A Project #2 – To Mars!
Richard The

## Slide 2: Setting Up the Solar System
Defined the properties of the planets & moons
Getting them to orbit correctly
Selecting a launch date
  With a launch date we set the start positions of the planets by using data from JPL horizon (http://www.jpl.nasa.gov/)
  Converted the data to polar coordinates to create an angle corresponding to each planets (and moons) start point.
  With this the planets where then updated to start at the corresponding starting angles and given distance so they mimic their positions on the given date.

## Slide 3: Setting Up the Launch
Calculated the acceleration due to the rockets thrust from its changing mass and changing velocity.
Determined the angle at which the space craft launched/rotates from.
Incorporation of air drag
  Found equations to determine the variables of air drag.
    Calculated the cross-sectional area of the Atlas V rocket to be that or a circle with a diameter 3.81 meters.
    Found the coefficient of drag to be 0.4, the coefficient of streamline model rockets (http://library.thinkquest.org/10568/aerodynamics/forces.html)
  Shut off the pressure equation at 44,300 meters so we would not get imaginary numbers.

## Slide 4: Formulas
Acceleration from a rocket :

## Slide 5: Atlas V-541

## Slide 6: Atlas V-541 (stage 1)
Aerojets (4)
  Fthrust = 1,270 kN
  mtotal = 40,820 kg
  mpropellant = 36,820 kg
  Burn Rate = 529 kg/s
  Isp = 245 seconds
CCB (Common Core Booster)
  Fthrust = 4,152 kN
  mtotal = 307,000 kg
  mfuel = 284,450 kg
  Burn Rate = 1,360.9 kg/s
  tburn = 253 seconds
  Isp = 311 seconds

## Slide 7: Atlas V-541 (stage 1)

## Slide 8: Atlas V-541 (stage 2)
Centaur
  Fthrust = 99.2 kN
  mtotal = 18,710 kg
  mfuel = 16,805 kg
  Burn Rate = 22.42 kg/s
  tburn = 738 seconds
  Isp = 451 seconds

## Slide 9: Atlas V-541 (stage 2)

## Slide 10: Atlas V-541 (stage 3)
Payload
  mass = 3,000 kg
    1,000kg “Curiosity” + accessories & landing craft
Total Fuel Used = 478,650 kg
Space Maneuvering Thruster (NK-43)
  vex = 3,248 m/s
  Fthrust = 1,753.8 kN
  Isp = 331 seconds
  mdry = 1,235 Kg

## Slide 11: NK-43
NK-33 and NK-43 are rocket engines designed and built in the late 1960s and early 1970s by the Kuznetsov Design Bureau. They were intended for the ill-fated Soviet N-1 rocket moon shot. The NK-33 engine achieves the highest thrust-to-weight ratio of any Earth-launchable rocket engine, whilst achieving a very high specific impulse. NK-33 is by many measures the highest performance LOX/Kerosene rocket engine ever created.
http://en.wikipedia.org/wiki/NK-33

## Slide 12: Distance from the Earth

## Slide 13: Distance from Mars

## Slide 14: Air Drag (Earth)

## Slide 15: Gravitational Potential Energy (Earth)

## Slide 16: Gravitational Potential Energy (Mars)

## Slide 17: Resources
http://www.jpl.nasa.gov/
http://www.spacelaunchreport.com/atlas5.html
http://library.thinkquest.org/10568/aerodynamics/forces.html
http://www.astronautix.com